## Slide 1: Microcontroller Assembly
Microcontroller Assembly Programing
By Rashed-2003023

## Slide 2: Introduction to Assembly Programming
  Binary and machine language challenges
  Hexadecimal system introduction
  Evolution to Assembly languages
  Mnemonics for human-friendly coding
  Low-level programming and CPU interaction
  Role of the assembler in translation
  Comparison with high-level languages
Key Message: Assembly languages bridge the gap between machine language and human-readable code.

## Slide 3: Assembly Language Structure
  An Assembly language instruction consists of four fields:
  label: mnemonic operands ; comment
  Important Points:
  1. The label field allows the program to refer to a line of code by name. The label field cannot exceed a certain number of characters.
  2. The comment field begins with a semicolon comment indicator ";". Comments may be at the end of a line or on a line by themselves. The assembler ignores comments, but they are indispensable to programmers.
  3.The Assembly language mnemonic (instruction) and operand(s) fields togeth­er perform the real work of the program and accomplish the tasks for which the program was written.
Example: LDI R23, $55
ADD R23, Rl9
SUBI R23, $67

## Slide 4: Sample of an Assembly Language Program
;AVR Assembly Language Program To Add Some Data.
;store SUM in SRAM location Ox300.
.EQU SUM Ox300 ;SRAM loc $300 for SUM
.ORG 00 ;start at address 0
LDI Rl6, 0x25 ; Rl6 0x25
LDI Rl7, $34 ; Rl7 0x34
LDI Rl8, Ob00110001 ; Rl8 0x31
ADD Rl6, Rl7 ;add Rl7 to Rl6
ADD Rl6, Rl8 ;add Rl8 to Rl6
LDI Rl7, 11 ;Rl7 = 0x0B
ADD Rl6, Rl7 ;add Rl7 to Rl6
STS SUM, Rl6 ;save the SUM in loc $300
HERE: JMP HERE ;stay here forever
Mnemonic
Label
Comment
Operands

## Slide 5: ASSEMBLING AN AVR PROGRAM
Editor Program
Assembler
Program
myfile.eep myfile.hex myfile.map myfile.lst myfile.obj
Download to AVR’s EEPROM
Download to
AVR’s FLASH
myfile.asm

## Slide 6: ASSEMBLING AN AVR PROGRAM
Editor Program: Used to write and modify code files; common ones include Notepad, Visual Studio Code, or Atmel Studio for AVR programming.
ASM File (Assembler Code): AVR assembly code written by the programmer, providing low-level instructions for the AVR microcontroller.
Assembler Program: Converts ASM code into machine code (binary), creating an OBJ file for AVR programs.
EEP File: Stands for Electrically Erasable Programmable Read-Only Memory; contains non-volatile data for the AVR's EEPROM, preserving data between power cycles.

## Slide 7: ASSEMBLING AN AVR PROGRAM
Hex File: Compiled machine code in hexadecimal format; loaded onto AVR microcontrollers for execution.
Map File: Offers a detailed map of memory usage, showing how program elements occupy space in the AVR's memory.
LST File: Lists the assembly instructions with corresponding memory addresses, aiding in program analysis and debugging.
OBJ File: Intermediate file generated by the AVR assembler, containing relocatable machine code before being linked to create the final HEX file for AVR microcontrollers.